## Slide 1
Data Processing Pipeline for Digital-Twin-Ready Geohazard Modeling
Raw event data → harmonized raster stacks → Landlab physics + ML learning/surrogates → fast scenario prediction
Event / AOI
fire ID AOI polygon date window
Raw Data Retrieval
LiDAR / DEM fire + landcover soils + forcing inventories
Geospatial Harmonization
clip AOI reproject CRS resample grid QA / nodata
Model-Ready Stack
aligned ASC + TIF features + labels tiles / chunks
Derived Features
slope curvature SCA / drainage cohesion / PFT
Staged Outputs
Landlab ML DT layers
Raw inputs
Terrain
DEM, LiDAR, pre/post elevation
Fire + LC
burn severity, perimeters, NLCD
Soils / Veg
soil depth, Ksat, texture, cohesion
Hydroclimate
NDVI, LAI, SWE, SMAP, precip/temp
Labels
landslides, debris-flow inventory
Downstream modeling routes
Route 1: Physics
Landlab process simulation runoff, routing, mass wasting evolving landscape state
Route 2: Observed ML
source detection segmentation / susceptibility terrain-change learning
Route 3: Surrogates
train on simulation ensembles approximate expensive Landlab fast uncertainty rollout
Route 4: Digital Twin Layer
connect forcing, observations, simulations, surrogate outputs iterative updates + decision support
Final Capability
fast, scalable, uncertainty-aware geohazard prediction for scenario modeling and digital-twin workflows
Compute Needs
CPU: orchestration + Landlab RAM/I/O: LiDAR + rasters GPU: ML + surrogates
Positioning: data infrastructure enables scalable physics simulation, observation-based learning, and surrogate acceleration.